# openWRT mit LTE
Router: tl-wr1043nd LTE-Stick: Vodafone 5005
- openwrt installieren
- opkg update
- Weitere Pakete installieren:
  opkg install libpthread kmod-mii kmod-usb-net kmod-usb-wdm kmod-usb-net-qmi-wwan librt libusb-1.0 usb-modeswitch uqmi
- reboot
- konfigure QMI
  - root@OpenWrt:~# ls -l /dev/cdc-wdm0
    crw-r--r-- 1 root root 180, 176 Oct 1 12:03 /dev/cdc-wdm0
  - Sollte der Stick nicht vorhanden sein:
    usbmode -l
    usbmode -s
  - root@OpenWrt:~# uqmi -d /dev/cdc-wdm0 --get-data-status
    "disconnected"
    root@OpenWrt:~# uqmi -d /dev/cdc-wdm0 --get-signal-info
    {
            "type": "lte",
            "rssi": -61,
            "rsrq": -6,
            "rsrp": -88,
            "snr": 290
    }
  - root@OpenWrt:~# uqmi -d /dev/cdc-wdm0 --start-network internet --autoconnect
    38750672
    root@OpenWrt:~# uqmi -d /dev/cdc-wdm0 --get-data-status
    "connected"
  - in /etc/config/network
    config interface 'wwan'
            option ifname 'wwan0'
            option proto 'dhcp'
  - Firewall-Regel; Network → Firewall; WAN-Interface → Edit; WWAN anhaken
# Quellen:
http://nucblog.net/2014/10/turn-your-old-wireless-router-into-an-lte-router-with-openwrt/