## Installation
sudo apt-get fail2ban sendmail
## Konfiguration
Erstellen der Config-Files
cp /etc/fail2ban/jail.conf /etc/fail2ban/jail.local
Konfigurations-File für fail2ban ist unter /etc/fail2ban/fail2ban.conf zu finden
# Fail2Ban configuration file # # Author: Cyril Jaquier # # $Revision: 629 $ # [Definition] # Option: loglevel # Notes.: Set the log level output. # 1 = ERROR # 2 = WARN # 3 = INFO # 4 = DEBUG # Values: NUM Default: 3 # loglevel = 3 # Option: logtarget # Notes.: Set the log target. This could be a file, SYSLOG, STDERR or STDOUT. # Only one log target can be specified. # Values: STDOUT STDERR SYSLOG file Default: /var/log/fail2ban.log # logtarget = /var/log/fail2ban.log # Option: socket # Notes.: Set the socket file. This is used to communicate with the daemon. Do # not remove this file when Fail2ban runs. It will not be possible to # communicate with the server afterwards. # Values: FILE Default: /var/run/fail2ban/fail2ban.sock # socket = /var/run/fail2ban/fail2ban.sock

Nachfolgendes File ist für die einzelnen blockbaren Dienste:
/etc/fail2ban/jail.local
# Fail2Ban configuration file. # # This file was composed for Debian systems from the original one # provided now under /usr/share/doc/fail2ban/examples/jail.conf # for additional examples. # # To avoid merges during upgrades DO NOT MODIFY THIS FILE # and rather provide your changes in /etc/fail2ban/jail.local # # Author: Yaroslav O. Halchenko <debian@onerussian.com> # # $Revision: 281 $ # # The DEFAULT allows a global definition of the options. They can be override # in each jail afterwards. [DEFAULT] # "ignoreip" can be an IP address, a CIDR mask or a DNS host ignoreip = 127.0.0.1 bantime = 86400 maxretry = 3 # "backend" specifies the backend used to get files modification. Available # options are "gamin", "polling" and "auto". # yoh: For some reason Debian shipped python-gamin didn't work as expected # This issue left ToDo, so polling is default backend for now backend = polling # # Destination email address used solely for the interpolations in # jail.{conf,local} configuration files. destemail = patrick.schindelmann@googlemail.com # # ACTIONS # # Default banning action (e.g. iptables, iptables-new, # iptables-multiport, shorewall, etc) It is used to define # action_* variables. Can be overriden globally or per # section within jail.local file banaction = iptables-multiport # email action. Since 0.8.1 upstream fail2ban uses sendmail # MTA for the mailing. Change mta configuration parameter to mail # if you want to revert to conventional 'mail'. mta = sendmail # Default protocol protocol = tcp # # Action shortcuts. To be used to define action parameter # The simplest action to take: ban only action_ = %(banaction)s[name=%(__name__)s, port="%(port)s", protocol="%(protocol)s] # ban & send an e-mail with whois report to the destemail. action_mw = %(banaction)s[name=%(__name__)s, port="%(port)s", protocol="%(protocol)s] %(mta)s-whois[name=%(__name__)s, dest="%(destemail)s", protocol="%(protocol)s] # ban & send an e-mail with whois report and relevant log lines # to the destemail. action_mwl = %(banaction)s[name=%(__name__)s, port="%(port)s", protocol="%(protocol)s] %(mta)s-whois-lines[name=%(__name__)s, dest="%(destemail)s", logpath=%(logpath)s] # Choose default action. To change, just override value of 'action' with the # interpolation to the chosen action shortcut (e.g. action_mw, action_mwl, etc) in jail.local # globally (section [DEFAULT]) or per specific section action = %(action_mwl)s # # JAILS # # Next jails corresponds to the standard configuration in Fail2ban 0.6 which # was shipped in Debian. Enable any defined here jail by including # # [SECTION_NAME] # enabled = true # # in /etc/fail2ban/jail.local. # # Optionally you may override any other parameter (e.g. banaction, # action, port, logpath, etc) in that section within jail.local [ssh] enabled = true port = ssh filter = sshd logpath = /var/log/auth.log maxretry = 4 # Generic filter for pam. Has to be used with action which bans all ports # such as iptables-allports, shorewall [pam-generic] enabled = false # pam-generic filter can be customized to monitor specific subset of 'tty's filter = pam-generic # port actually must be irrelevant but lets leave it all for some possible uses port = all banaction = iptables-allports port = anyport logpath = /var/log/auth.log maxretry = 6 [xinetd-fail] enabled = false filter = xinetd-fail port = all banaction = iptables-multiport-log logpath = /var/log/daemon.log maxretry = 2 [ssh-ddos] enabled = false port = ssh filter = sshd-ddos logpath = /var/log/auth.log maxretry = 6 # # HTTP servers # [apache] enabled = false port = http,https filter = apache-auth logpath = /var/log/apache*/*error.log maxretry = 6 # default action is now multiport, so apache-multiport jail was left # for compatibility with previous (<0.7.6-2) releases [apache-multiport] enabled = false port = http,https filter = apache-auth logpath = /var/log/apache*/*error.log maxretry = 6 [apache-noscript] enabled = false port = http,https filter = apache-noscript logpath = /var/log/apache*/*error.log maxretry = 6 [apache-overflows] enabled = false port = http,https filter = apache-overflows logpath = /var/log/apache*/*error.log maxretry = 2 # # FTP servers # [vsftpd] enabled = true port = ftp,ftp-data,ftps,ftps-data filter = vsftpd logpath = /var/log/vsftpd.log # or overwrite it in jails.local to be # logpath = /var/log/auth.log # if you want to rely on PAM failed login attempts # vsftpd's failregex should match both of those formats maxretry = 4 [proftpd] enabled = false port = ftp,ftp-data,ftps,ftps-data filter = proftpd logpath = /var/log/proftpd/proftpd.log maxretry = 6 [wuftpd] enabled = false port = ftp,ftp-data,ftps,ftps-data filter = wuftpd logpath = /var/log/auth.log maxretry = 6 # # Mail servers # [postfix] enabled = false port = smtp,ssmtp filter = postfix logpath = /var/log/mail.log [couriersmtp] enabled = false port = smtp,ssmtp filter = couriersmtp logpath = /var/log/mail.log # # Mail servers authenticators: might be used for smtp,ftp,imap servers, so # all relevant ports get banned # [courierauth] enabled = false port = smtp,ssmtp,imap2,imap3,imaps,pop3,pop3s filter = courierlogin logpath = /var/log/mail.log [sasl] enabled = false port = smtp,ssmtp,imap2,imap3,imaps,pop3,pop3s filter = sasl logpath = /var/log/mail.log # DNS Servers # These jails block attacks against named (bind9). By default, logging is off # with bind9 installation. You will need something like this: # # logging { # channel security_file { # file "/var/log/named/security.log" versions 3 size 30m; # severity dynamic; # print-time yes; # }; # category security { # security_file; # }; # } # # in your named.conf to provide proper logging # Word of Caution: # Given filter can lead to DoS attack against your DNS server # since there is no way to assure that UDP packets come from the # real source IP [named-refused-udp] enabled = false port = domain,953 protocol = udp filter = named-refused logpath = /var/log/named/security.log [named-refused-tcp] enabled = false port = domain,953 protocol = tcp filter = named-refused logpath = /var/log/named/security.log

## Server starten
sudo /etc/init.d/fail2ban start